## Slide 1
TCP/IP Programming
Joel Snyder, Opus One
Geoff Bryant, Process Software
Portions Copyright © 1996 TGV Software, Inc.,
Copyright © 1996 Process Software Corp.
Copyright © 1996 Opus1

## Slide 2
Course Roadmap
NM055 (11:00-12:00) Important Terms and Concepts
  TCP/IP and Client/Server Model
  Sockets and TLI
  Client/Server in TCP/IP
NM056 (1:00-2:00) Socket Routines
NM057 (2:00-3:00) Library Routines
NM058 (3:00-4:00) Sample Client/Server
NM059 (4:00-5:00) VMS specifics (QIOs)
NM067 (6:00-7:00) Clinic - Q&A

## Slide 3
TCP/IP Programming
Slides and Source Code available via anonymous FTP:
Host:: ftp.process.com
Directory: [pub.decus]
Slides: DECUS_F96_PROG.PS
Examples: DECUS_F96_PROG_EXAMPLES.TXT
Host: ftp.opus1.com
Directory: [.decus]
Slides: DECUS_F96_PROG.POWERPOINT
Examples: DECUS_F96_PROG_EXAMPLES.TXT

## Slide 4
Session NM055 TCP/IP Programming Terms and Concepts Joel Snyder Opus One

## Slide 5
Terms and Concepts Overview
What is the TCP/IP model?
What is the client/server model?
What are sockets and TLI?
What is network byte order?
What is encapsulation? Multiplexing? Demultiplexing? Fragmentation?
What are addresses?

## Slide 6
Networks are layered to simplify construction
Data Link
Physical
Network
Transport
Session
Presentation
Application
Data Link
Physical
Network
Data Link
Physical
Network
Transport
Session
Presentation
Application
The Famous OSI 7-Story Apartment Building with attached Parking Garage

## Slide 7
The OSI Model (similar to the Holy Grail)
Physical
Data Link
Network
Transport
Session
Presentation
Application
Transmission of binary data of a medium
Transfer of units of information, framing, and error checking
Delivery of packets of information, which includes routing
Provision for end-to-end reliable and unreliable delivery
Establishment and maintenance of sessions
Data formatting and encryption
Network applications such as file transfer and terminal
emulation
OSI layer
Function provided
Notes: Developed by the International Organization for Standardization in 1974 as a model for data communications system.
It consists of seven layers.
Each layer has a different but specific processing function.
The whole model constitutes the individual pieces needed to construct a network.
Each layer provides functions for the layer directly adjacent to it.
Modules (layers) may be replaced with one of equal type (that is, transport layer may not be replaced with the network layer).
Being familiar with the OSI model allows for a more complete understanding of a network.

## Slide 8
TCP/IP is (usually) sliced up into four layers
Data Link/Physical
Network
Transport
Application
Network
Network
Transport
Application
There are actually more layers to TCP/IP than this set of four, but from the programming point of view, this will do just fine.
Data Link/Physical
Data Link/Physical

## Slide 9
We care most about the two center layers
Application
TCP
(Transmission Control Protocol)
UDP
(User Datagram Protocol)
IP
(Internet Protocol)
hardware interface
Application
Application
Application
Transport
Network
Physical/Data Link

## Slide 10
TCP
Transmission Control Protocol is defined by RFC-793
TCP provides connection-oriented transport service
End-to-end transparent byte-stream

## Slide 11
UDP
User Datagram Protocol is defined by RFC-768
UDP provides datagram service
Connectionless

## Slide 12
Client/Server is application-to-application
TCP/IP and DECnet are client/server networks
A client/server application has two parts
  One which runs on one side of the network
  One which runs on the other side of the network
Differentiate this from a terminal-based network or most Netware applications

## Slide 13
Clients and Servers use IPC to talk to each other
Inter-Process Communication mechanisms let two cooperating applications communicate
There are LOTS of IPC mechanisms for local communications
The two popular TCP/IP based IPCs are Sockets (Berkeley Unix) and TLI (AT&T Unix System V)
Notes: We’re going to defer the discussion of TLI essentially forever. Although we won’t be mentioning TLI, this doesn’t imply that it’s not useful or important. However, Multinet does not support the TLI API; instead, it supports Sockets (and a bunch of other VMS-specific APIs which are ALSO not going to be covered in this course.
Other examples of IPCs: mailboxes, shared memory (via global sections), disk files, named pipes.

## Slide 14
Sockets is the standard API for TCP/IP IPC
Normally, you’d have an operating system specific routine set to talk to the network
In the world of standardized APIs, you would have an operating system independent set of routines
Sockets takes it one step further: it makes the network look much like a file system

## Slide 15
TCP/IP is a file system?
Routines to open up a file
Routines to close an open file
Routines to open up a connection
Routines to close an open connection
Read
Write
Yes, sockets treats TCP/IP as if it were a file system
(with some added complexity in the open and close routines)

## Slide 16
It looks like a file, but it’s really a network interface
Application
Application
write()
read()
write()
read()

## Slide 17
Life was easy when machines had 8-bit words
Welcome to the concept of “network byte order”
Remember that “network byte order” is not the same as “host byte order”
You have to convert to network byte order!

## Slide 18
There are two ways to store multi-byte integers
high order byte
high order byte
low order byte
low order byte
Address n
Address n
Address n+1
Address n+1
big endian
little endian

## Slide 19
VMS systems are little endian architectures
Big-endian architectures
Little-endian architectures
Motorola 68xxx
IBM 370
Intel 80x86
VAX & Alpha (VMS)
PDP-11(sort of)
0 1 2 3
3 2 1 0
Notes: Do you have to memorize this table?
NO! The point is that you need tooknow that there are little-endian and big-endian systems. You have one or the other. There are also routines which let you convert from “HOST” byte order to “NETWORK” byte order. You simply have to remember to use them when you’re doing any TCP/IP header manipulation.
On a Big-endian machine, these routines are essentially NO-OPs. On little-endian machines, these routines do the conversion you need. Always call them or you will write bad code ! ! !

## Slide 20
Relax: you could be doing Ethernet and Token Ring
. . . .
Byte 0
Byte 1
Byte 5
Byte 0
Byte 1
Byte 5
Source address
Bit 0
Bit 0
Bit 7
Transmitted first
Bit 7
Transmitted first
Destination address
Type field
6 bytes
6 bytes
2 bytes
46 - 1500
bytes
4 bytes
Multicast bit
LSB
MSB
M
. . . .
Transmission
sequence
Destination
address
Source
address
Data
field
Frame
Check
Sequence
Bits within bytes are
transmitted left to right

## Slide 21
Encapsulation adds control information to data
Trailers
Headers
Now is the time for all good
File server
Client workstation
Headers
Trailers
Request block of data
Request
Response
Data field
Data from user program such as an application
program or session control information
Network
headers
Network
trailers
men to come to the aid of
Response
of their country
Response
Headers
Headers
Trailers
Trailers
Now is the time
for all good men
to come to the
aid of their
country
Notes: Packets
Network stations communicate through the use of packets.
  There are different packet types depending on the access method and network software that is used.
Packets have a maximum and minimum size and a definite beginning and ending.
Generally, the format of the packet is:
  network headers, a data field, and network trailers.
    Network headers and trailers are placed in there by the network hardware or software.
For example:
  A network station requests a block of data from its file server.
    The network station builds a request packet and transmits it to the network.
    The file server receives this request and builds response packets (more data is sent than one packet can hold).
    The file server sends the response packets back to the requesting network station.

## Slide 22
Each layer encapsulates the layer below it
Physical
Data Link
Network
Transport
Session
Presentation
Application
Data link
header
Network layer
header
Transport layer
header
Session layer
header
Presentation and
Application layer
header
OSI model
Network packet
Data link
trailers
Notes: OSI Layers as Packet Headers
Each OSI layer that is represented in the network software or hardware adds its respective header or trailer to the packet.
When the packet is received at the remote end of a connection this header and trailer information is stripped off by the same OSI layer software.
For example, the transport layer software processes only the transport layer header in the packet.
  The other layers will process their headers and leave the other headers or trailers alone.
The maximum and minimum packet size for any network does not increase for the placement of the network header or trailers.
  It uses the existing data field of the packet to place their information.

## Slide 23
Things can be added on and peeled off at the ends
Application Layer Data
Application Layer Data
Application Layer Data
Application Layer Data
Application Layer Data
Look at your average WWW query
HTTP header
HTTP header
HTTP header
HTTP header
TCP header
TCP header
TCP header
IP header
IP header
Ethernet header
Ethernet trailer
14
20
20
192
4

## Slide 24
Make sure you memorize all of this encapsulation info
Destination
address
Source
address
Type
field
Data field
CRC
Destination
address
Source
address
Length
field
Data field
CRC
Destination
address
Source
address
Length
field
DSAP
SSAP
CTRL
Data field
CRC
SNAP header
Destination
address
Source
address
Length
field
Data field
CRC
FFFF
Destination
address
Source
address
Length
field
DSAP
SSAP
CTRL
Data field
CRC
OUI
Ethernet V2.0
IEEE 802.3
IEEE 802.3 with IEEE 802.2
IEEE 802.3 SNAP
Novell proprietary
6 bytes
2 bytes
Up to 1500 bytes
4 bytes
Up to 1496 bytes
6 bytes
6 bytes
6 bytes
4 bytes
4 bytes
2 bytes
4 bytes
6 bytes
6 bytes
1 byte
1 byte
*
4 bytes
2 bytes
6 bytes
6 bytes
Up to 1500 bytes
6 bytes
6 bytes
2 bytes
1 byte
1 byte
3 bytes
2 bytes
1492 bytes
FDDI
Token Ring
Destination
address
Source
address
Length
field
DSAP
SSAP
CTRL
Data field
4 bytes
6 bytes
6 bytes
2 bytes
1 byte
1 byte
4472 bytes
EtherType
Preamble
SD
FC
FCS
FS
ED
1 byte
1 byte
Destination
address
Source
address
DSAP
SSAP
CTRL
Data field
CRC
4 bytes
6 bytes
6 bytes
1 byte
1 byte
4472 (4 Mbps or 17800 (16 Mbps) bytes
RIF
SD
AC
FC
FS

## Slide 25
Multiplexing and Demultiplexing
Application Process
Application Process
Application Process
TCP
UDP
IP
Ethernet interface
Ethernet interface
IPX
DECnet
Notes: A user process may use different protocols at the same time. For example, one process is using both TCP & UDP
More than one process can be using each protocol at a time. This requires that the protocol (such as TCP) identify the process that’s sending data down/up. This is MULTIPLEXING. In the other direction, data going up, this is DEULTIPLEXING. We’ll talk about addressing which handles this in a few slides.
The IP module has to determine whether data is to be demuultiplexed from the 2 Ethernet interfaces to which of the UDP/TCP modules.
Ethernet also multiplexes/demultiplexes to other protocols, such as DECnet or LAT.

## Slide 26
Segmentation and Reassembly
Application Data Message
TCP
IP
TCP
IP
TCP Segments
IP Packets

## Slide 27
Addressing identifies entities in the network
Each layer in a TCP/IP stack has an address made up of two parts
  The address of everything below it
  The address of itself
In some cases, lower-level addresses are implied and do not have to be stated
  For example, Ethernet MAC addresses are tied directly to IP addresses, so they can be omited

## Slide 28
Three addresses are important: IP, Protocol, Port
Application-level addresses
Transport-level addresses
Network-level addresses

## Slide 29
IP addresses are 32-bit integers
Application-level addresses
Transport-level addresses
Network-level addresses
IP Address: 192.245.12.2

## Slide 30
Transport addresses are 8-bit protocol numbers
Application-level addresses
Transport-level addresses
Network-level addresses
Protocol Number:
TCP = 6
UDP=17

## Slide 31
Port Numbers are 16-bit integers
Application-level addresses
Transport-level addresses
Network-level addresses
Port Number: SMTP = 25
Notes: A mechanism to multiplex access to the network layer
TCP and UDP use 16-bit numbers, called “ports”.
Network software matches particular ports with associated processes

## Slide 32
The triplet (IP,Proto,Port) identifies a process
IP number (network address)
Protocol number (transport address)
Port number (application address)

## Slide 33
Two triplets identify a connection
Now we have a socket!
  (sometimes called a “socket pair”)
Application number 1117
on protocol number 6 (TCP)
at IP address 192.245.12.2
Application number 25
on protocol number 6 (TCP)
at IP address 128.196.128.233

## Slide 34
A socket maps one application to another
Application Process
Application Process
TCP
UDP
IP
Ethernet interface
Application Process
TCP
UDP
IP
Ethernet interface
1117
25
6
6
192.245.12.2
128.196.128.233

## Slide 35
Addresses are assigned by different entities
IP addresses are assigned by the InterNIC and are managed by the local network manager
Protocol numbers are assigned by the IANA (Internet Assigned Number Authority) and are fixed across the Internet (RFC 1700)
Application port numbers come from two sources
  Servers are assigned by IANA (RFC 1700)
  Clients are handled by the network kernel

## Slide 36
IP Addressing
IP is the Internet Protocol, currently version 4
IPNG is the Next Generation (also known as IPv6)
IP is defined by RFC-791
IP uses four octet (8-bit byte) addresses
IP takes care of getting packets to destination

## Slide 37
Client and Server Port Numbers are coordinated
NORMALLY, Server port numbers are low numbers in the range 1-1023
  Defined in RFC 1700
NORMALLY, Client port numbers are high numbers starting at 1024
  These are called “ephemeral ports”

## Slide 38
You only pick server ports
A server running on a “well-known port” lets the operating system know what port it wants to listen on
A client simply lets the operating system pick a new port (ephemeral) that isn’t already in use

## Slide 39
Well-Known-Servers
Public services (e.g. and email server) are assigned a particular number by IANA
These numbers are stored in the Internet Assigned Numbers RFC (changing number, latest is 1700)
These are called Well-Known-Servers
Examples of these include TELNET (23), SMTP (25), FINGER (79), HTTP (80), RLOGIN (512) and others

## Slide 40
Important Terms Key Concepts
TCP/IP networks are layered
TCP/IP uses a client/server paradigm
Addressing triples (IP, protocol, port) identify applications in TCP/IP
A pair of triples beats a full house

## Slide 41
Client/Server in TCP/IP

## Slide 42
Client/Server in TCP/IP Overview
What is the server process (INETD)?
What are ephemeral ports?
How can you have multiple connections?
How are processes identified?
What is Connection-oriented? Connection-less?

## Slide 43
Making the initial connection to a server
When a connection enters a TCP/IP system, someone has to handle it
  Either a running daemon is waiting (your application)
  or a running daemon is waiting (InetD)
Trade off efficiency for performance
  Choose whichever model you want based on individual application characteristics
  Seldom used? Inetd
  Constantly used? True Daemon

## Slide 44
Your application can wait for an incoming connection
This is called the “Daemon” (or Demon) approach
Your Application
Network Kernel
If anything should come in for Port 25 on TCP, give it to me. I will be waiting right here.
OK.

## Slide 45
Or you can have the InetD do it for you
Your Application
Network Kernel
Here’s an incoming call.
Port 25? I will start a new process running Your Application and hand it this incoming call.
InetD
In Multinet, InetD is known as the Master Server
In TCPware, InetD is part of NETCP
In UCX, InetD is the Auxilliary Server

## Slide 46
Servers low, Clients high
Servers:ports 1-1023
Clients:
“ephemeral ports” above 1023

## Slide 47
A Server may connect to multiple clients
Each connection is a pair of triples (IP, protocol, port)
The server side may remain the same across multiple clients
Of course, the server programmer has to keep it all straight

## Slide 48
Socket-pairs leave no ambiguity between 2 clients
Client
TCP
IP
Ethernet interface
SERVER
TCP
IP
Ethernet interface
1117
25
6
6
192.245.12.2
128.196.128.233
Client
TCP
IP
Ethernet interface
5555
6
195.240.3.1

## Slide 49
Applications are known by their port numbers
A process is identified by its 16-bit port number
If a server uses both TCP and UDP, it will often use the same port number for both protocols
  Protocol number means no ambiguity
The concept of low-numbered ports as “privileged” disappeared with PCs
  Don’t base your security on port numbers!
Some services use a meet-me approach

## Slide 50
TCP/IP supports CL and CO at transport layer
CO = Connection Oriented
  TCP
  “Stream”
CL = Connectionless
  UDP
  “Datagram”
CL can be provided by pure IP
  Unusual
  “Raw”

## Slide 51
Connection oriented is like a phone call
Connection oriented data communications arrived before connectionless
  Used primarily over noisy serial lines in original intention.
    not necessarily an issue with TCP
  Two stations must establish a connection before data is transmitted.
  Connection is strictly maintained using sequence numbers, acknowledgments, retries and so on.

## Slide 52
Connect, Transfer, Disconnect
Connect Request
Connect Confirm
Data
Disconnect Request
Disconnect Confirm
Note: This is almost like how it’s done in TCP. Take the internals course for more info.

## Slide 53
Connectionless is like a postcard
Connectionless allows data to be transmitted without a pre-established connection between two stations.
  This type of service flourished with the proliferation of LANs.
    LANs tend to have a very low error rate and a connection need not be established to ensure the integrity of the data.
  This type of service does not provide error recovery, flow or congestion control.
    upper layer network protocols can accomplish this.
  It requires less overhead and is implicitly faster.

## Slide 54
Nike style data communications
Data
Note: This is exactly like how it’s done in UDP. Take the internals course for more info.
Data
Data
Data

## Slide 55
Client/Server in TCP/IP Key Concepts
Servers are handled in one of two ways: resident daemons or InetD
Server ports are low-numbers; client ports are high-numbered ephemeral ports
A server can talk to many clients if the programmer can keep them straight
TCP is CO; UDP is CL

## Slide 56
Session NM056 Programming TCP/IP with Sockets Geoff Bryant Process Software

## Slide 57
Course Roadmap
NM055 (11:00-12:00) Important Terms and Concepts
  TCP/IP and Client/Server Model
  Sockets and TLI
  Client/Server in TCP/IP
NM056 (1:00-2:00) Socket Routines
NM057 (2:00-3:00) Library Routines
NM058 (3:00-4:00) Sample Client/Server
NM059 (4:00-5:00) VMS specifics (QIOs)
NM067 (6:00-7:00) Clinic - Q&A

## Slide 58
TCP/IP Programming
Slides and Source Code available via anonymous FTP:
Host:: ftp.process.com
Directory: [pub.decus]
Slides: DECUS_F96_PROG.PS
Examples: DECUS_F96_PROG_EXAMPLES.TXT
Host: ftp.opus1.com
Directory: [.decus]
Slides: DECUS_F96_PROG.POWERPOINT
Examples: DECUS_F96_PROG_EXAMPLES.TXT

## Slide 59
Programming with Sockets Roadmap
Berkeley Socket History
Overview of the Socket Paradigm
Socket addresses
Other programming models

## Slide 60
Berkeley Socket History
Documented in such books as
  Stevens’s Unix Network Programming
  Comer’s Internetworking with TCP/IP, vol III
First provided with Berkeley Software Distribution (BSD 4.1c) Unix for the VAX
Popularized in the 1986 4.3BSD release

## Slide 61
Other Programming Models
Socket model is widely used
  mainly due to wide implementation of BSD networking kernel
  Avaible for Unix, Windows, VMS, ...
Other models may be used in different environments
  STREAMS model (UNIX System V)
  Others

## Slide 62
Socket Paradigm Overview
A socket is a communications endpoint
In BSD networking, it is a data structure within the kernel
A socket is “named” by its socket address
A connection is represented by two communicating sockets

## Slide 63
Using sockets is like using the file system
Server
bind()
listen()
accept()
socket()
connect()
write()
read()
close()
read()
socket()
write()
connection establishment
block until connection from client
Client
close()

## Slide 64
Servers sit in a tight loop
bind()
listen()
accept()
close()
read()
socket()
write()
Notes: An example of socket system calls made by a simple server using TCP. The server runs forever, waiting for new connections on the well-known port. It accepts each new connection, processes the request from the client, and then closes the connection.

## Slide 65
Connectionless Client/Server is simpler
Server
bind()
socket()
sendto()
recvfrom()
socket()
Client
bind()
block until data from client
sendto()
recvfrom()

## Slide 66
A socket is just a data structure
Protocol Family
Service
Local Address
Remote Address
Operating System Channel List
socket

## Slide 67
In C, a socket doesn’t have much
Protocol Family
Service
Local Address
Remote Address
socket
integer: always set to be PF_INET for TCP/IP programming
integer: set to be SOCK_STREAM (TCP), SOCK_DGRAM (UDP), or SOCK_RAW (raw IP)
sockaddr: a 2-octet address family identifier and then 14 octets of address-specific information

## Slide 68
Families and Types
Address Families (or Protocol Families)
  AF_UNIX: Unix domain sockets
  AF_INET: Internet Protocols
  AF_NS: Xerox NS Protocols
  AF_IMPLINK: IMP link layer (obsolete)
Types:
  SOCK_STREAM: Stream socket (TCP)
  SOCK_DGRAM: Datagram socket (UDP)
  SOCK_RAW: Raw socket (IP)

## Slide 69
TCP/IP addresses are special cases of sockaddr
Protocol Family
Service
Local Address
Remote Address
socket
sockaddr: a 2-octet address family identifier and then 14 octets of address-specific information
struct sockaddr_in {
u_short sin_family;
u_short sin_port;
struct in_addr sin_addr;
char sin_zero[8];
}
struct sockaddr {
u_short sa_family;
char sa_data[16];
}

## Slide 70
sockaddr unveiled
struct sockaddr_in {
u_short sin_family;
u_short sin_port;
struct in_addr sin_addr;
char sin_zero[8];
}
sin_family: AF_INET for all TCP/IP addresses
sin_port: 16-bit port number (as used in UDP & TCP headers)
sin_addr: 32-bit IP address
/*
* Internet address (a structure for historical reasons)
*/
struct in_addr {
union {
struct { u_char s_b1,s_b2,s_b3,s_b4; } S_un_b;
struct { u_short s_w1,s_w2; } S_un_w;
u_long S_addr;
} S_un;
#define s_addr S_un.S_addr

## Slide 71
Remember our goal: open()
TCP/IP socket programming is mostly read() and write() subroutine calls
All of the socket routines are there to do the equivalent of an open() in the file system.

## Slide 72
Five routines are used to replace the open() call
Protocol Family
Service
Local Address
Remote Address
socket
socket() : allocate socket in memory, fill in protocol family and service fields
bind(): fill in the local address part (local sockaddr). OPTIONAL for most clients
listen(): tell network kernel that you want to receive connects (“passive open”)
accept(): ask network kernel to hand you the next incoming connect (“passive open”)
connect(): tell network kernel to connect to the other side (“active open”)

## Slide 73
Overview of Sockets (one more time)
Get the socket open somehow
  socket(), bind(), listen(), accept(), connect()
Read and write from it
  read(), write()
When done, close the socket
  close()

## Slide 74
Programming with Sockets Key Concepts
A socket is a data structure representing a connection
To open a connection
  Fill in the data structure
  Link it to the network kernel
  Link it to the operating system
Reading and writing uses the same calls as the file system

## Slide 75
Coding with Sockets

## Slide 76
General Flow for Servers/Clients is different
Server
bind()
listen()
accept()
socket()
connect()
write()
read()
close()
read()
write()
connection establishment
block until connection from client
Client
close()
socket()
Let’s start with clients because they’re easier

## Slide 77
Clients

## Slide 78
Step 1: Get Socket
socket()
connect()
write()
read()
close()
int socket(int domain, int type, int protocol);
int s, domain, type, protocol;
domain = AF_INET; /* always the same */
type = SOCK_STREAM; /* STREAM for TCP */
protocol = 0;
s = socket(domain, type, protocol);
if (s < 0) ERROR(“Cannot create socket”);

## Slide 79
Step 2: Fill in remote address fields
socket()
connect()
write()
read()
close()
#define SMTP_PORT 25
#define IP_ADDRESS 0xC0F50C02 /*192.245.12.2*/
struct sockaddr_in sin;
sin.sin_family = AF_INET;
sin.sin_port = htons(SMTP_PORT);
sin.sa_addr = htonl(IP_ADDRESS);

## Slide 80
Step 3: Connect to other side
socket()
connect()
write()
read()
close()
int connect(int s, struct sockaddr*name, int namelen);
int status;
status = connect(s, (struct sockaddr*)sin, sizeof(sin));
if (status != 0)
ERROR(“Cannot connect to other side”);

## Slide 81
Step 4: Use the socket
socket()
connect()
write()
read()
close()
char buf[LINELEN+1];
/*
* Now go into a loop, reading data from the network, writing
* it to the terminal and reading data from the terminal,
* writing it to the network...
*/
while ( (n = read(s, buf, LINELEN) ) > 0) {
fwrite(buf, n, 1, stdout);
if (!fgets(buf, LINELEN, stdin)) break;
write(s, buf, strlen(buf));
}
if (n < 0) {
ERROR(“Cannot read from socket!”);
}

## Slide 82
Step 5: Shut it down when done
socket()
connect()
write()
read()
close()
status = close(s);
if (status != 0)
ERROR(“Can not close socket”);

## Slide 83
Servers

## Slide 84
Server Review and Overview
bind()
listen()
accept()
close()
read()
write()
socket()
socket() : allocate socket in memory, fill in protocol family and service fields
bind(): fill in the local address part (local sockaddr). OPTIONAL for most clients
listen(): tell network kernel that you want to receive connects (“passive open”)
accept(): ask network kernel to hand you the next incoming connect (“passive open”)

## Slide 85
Step 1: Get Socket
int socket(int domain, int type, int protocol);
int s, domain, type, protocol;
domain = PF_INET; /* always the same */
type = SOCK_STREAM; /* STREAM for TCP */
protocol = 0;
s = socket(domain, type, protocol);
if (s < 0) ERROR(“Cannot create socket”);
bind()
listen()
accept()
close()
read()
write()
socket()
This should look vaguely familiar...

## Slide 86
Step 2: Fill in local address fields
bind()
listen()
accept()
close()
read()
write()
socket()
INADDR_ANY is a shorthand way of saying “I don’t care what the local address is”...
#define SMTP_PORT 25
#define IP_ADDRESS 0xC0F50C02 /*192.245.12.2*/
struct sockaddr_in sin;
sin.sin_family = AF_INET;
sin.sin_port = htons(SMTP_PORT);
sin.sa_addr = INADDR_ANY;

## Slide 87
Step 3: “Bind” address to the socket
bind()
listen()
accept()
close()
read()
write()
socket()
INADDR_ANY is a shorthand way of saying “I don’t care what the local address is”...
int bind(int s, struct sockaddr*name, int namelen);
int status;
status = bind(s, (struct sockaddr*)sin, sizeof(sin));
if (status != 0)
ERROR(“Cannot bind to local address”);

## Slide 88
Step 4: Tell the kernel to listen
bind()
listen()
accept()
close()
read()
write()
socket()
#define MAX_BACKLOG 5
int listen(int s, int backlog);
int status;
status = listen(s, MAX_BACKLOG);
if (status != 0)
ERROR(“Cannot ask kernel to listen”);

## Slide 89
Step 5: Block waiting for connect
bind()
listen()
accept()
close()
read()
write()
socket()
int accept(int s, struct sockaddr *addr, int *addrlen);
int status, addrlen, vs;
struct sockaddr_in sin2;
addrlen = sizeof(sin2);
vs = accept(s, (struct sockaddr*)&sin2, &addrlen);
if (vs < 0)
ERROR(“Cannot accept a connection.”);

## Slide 90
Step 6: Read and Write
bind()
listen()
accept()
close()
read()
write()
socket()
/* Get the line from the client. */
read ( vs, buf, 256 );
/* Translate the logical name. */
log_name = getenv ( buf );
/* Get the definition string and add a new line to it. */
sprintf ( buf, "%s\n", log_name );
/* Write the translation to the client. */
write ( vs, buf, strlen ( buf ) );
Yes, this code has lots of holes in it. But you get the picture of what we’re trying to do.

## Slide 91
Step 7: Tear down when done
bind()
listen()
accept()
close()
read()
write()
socket()
status = close(s);
if (status != 0)
ERROR(“Can not close socket”);

## Slide 92
Of course, there are more routines than those
socket
connect
write
read
close
bind
listen
accept
recv, recvmsg
recvfrom
send, sendmsg
sendto
shutdown
getpeername
getsockopt
setsockopt
Create a descriptor for use in network communication
Connect to a remote peer (client)
Send outgoing data across a connection
Acquire incoming data from a connection
Terminate communication and deallocate a descriptor
Bind a local IP address and protocol port to a socket
Place the socket in passive mode and set backlog
Accept the next incoming connection (server)
Receive the next incoming datagram
Receive the next incoming datagram and record source addr.
Send an outgoing datagram
Send an outgoing datagram to a particular dest. addr.
Terminate a TCP connection in one or both directions
After a connection arrives, obtain remote machine’s address
Obtain the current options for a socket
Change the options for a socket

## Slide 93
Coding with Sockets Key Concepts
All clients and servers basically look the same
Follow a template, but make sure you understand what you’re doing
  Lots of templates are wrong
  Lots of templates don’t do what you think they do

## Slide 94
Session NM057 Library Routines Joel Snyder Opus One

## Slide 95
Course Roadmap
NM055 (11:00-12:00) Important Terms and Concepts
  TCP/IP and Client/Server Model
  Sockets and TLI
  Client/Server in TCP/IP
NM056 (1:00-2:00) Socket Routines
NM057 (2:00-3:00) Library Routines
NM058 (3:00-4:00) Sample Client/Server
NM059 (4:00-5:00) VMS specifics (QIOs)
NM067 (6:00-7:00) Clinic - Q&A

## Slide 96
Library Routines Roadmap
The byteorder routines
The inet routines
The /etc/* database routines

## Slide 97
Byte order routines give machine independence
Remember that network byte order is not necessarily the same as host byte order
Always use byteorder routines when you want to look inside of protocol headers or call protocol routines
What you do in your own code for byte order is up to you
  If you are moving strange things (not ASCII) over the network, you should be using RPC/XDR

## Slide 98
Byte Order converts 16 and 32 bit quantities
#include <sys/params.h>
u_long htonl(u_long hostlong); /* converts 32-bit host to 32-bit network*/
u_short htons(u_short hostshort); /* converts 16-bit host to 16-bit network */
u_long ntohl(u_long netlong); /* converts 32-bit network to 32-bit host */
u_short ntohs(u_short netshort); /* converts 16-bit network to 16-bit host */

## Slide 99
Inet routines manipulate Internet addresses
Internet addresses are expressed often as character strings (e.g., “192.245.12.2”)
Internet addresses internally are all numbers (e.g., 0xABADF00D)
Inet routines convert between the two (and do other things)

## Slide 100
2 most important ones: inet_addr and inet_ntoa
#include <sys/socket.h>
#include <netinet/in.h>
#include <arpa/inet.h>
u_long inet_addr(char *cp); /* convert string 192.245.12.2 to number */
char * inet_ntoa(struct in_addr in); /* convert number to string */
Calling Sequence:
Example:
/* We have the IP address in the character array pointed to by host */
address = inet_addr(host);
if (address == INADDR_NONE) {
printf(“Your host name %s is not well formed.\n”, host);
return FALSE;
}

## Slide 101
Converting names is not the same as converting strings
inet_addr() and inet_ntoa() convert “192.245.12.2” and 0x0BADF00D back and forth.
  This is purely a mechanical operation
What about converting “Tennis.Opus1.COM” to a number?
  Now we have to go to the network databases

## Slide 102
In early TCP/IP world, network databases are files
List of all hosts in the world
List of all networks in the Internet
List of all protocols on this system
List of all services on this system
/etc/hosts
/etc/networks
/etc/protocols
/etc/services
What are we keeping track of?
Where are we storing it?

## Slide 103
The Domain Name System helped a lot!
List of all hosts in the world
List of all networks in the Internet
List of all protocols on this system
List of all services on this system
on the network!
<not used any more>
/etc/protocols
/etc/services
What are we keeping track of?
Where are we storing it?

## Slide 104
Ob: TCPware-specific info
Local information - can edit these files:
  TCPWARE:HOSTS. - local host definitions; initialized during configuration
  TCPWARE:SERVICES. - initial defaults
  TCPWARE:PROTOCOLS. - initial defaults
  TCPWARE:NETWORKS. - initial defaults
DNS client process provides this information to applications
DNS client automatically updated when files are edited

## Slide 105
Ob: Multinet-specific info
multinet:hosts.local has your local additions to hosts, networks, protocols, services
$ multinet host_table compile
$ @multinet:install_databases
hosts.services has TGV’s list of hosts, networks, protocols, services - Don’t Touch!
hosts.txt was for Milnet host tables. Should not be of any interest to anyone anymore.
network_database.
hosttbluk.dat
These two files (installed as global sections) plus the DNS (if used on your system) are used to answer queries from local applications.

## Slide 106
Translating names to addresses
Goal is to have IP address in a 32-bit quantity
We can start with either a domain name, e.g. Hearts.ACES.COM, or an IP address, e.g. 198.102.68.2
We can also take service, protocol, and network names and convert them to the relevant structures, e.g. TELNET, FTP, etc.

## Slide 107
Retrieve information from databases with routines
List of all hosts in the world
List of all networks in the Internet
List of all protocols on this system
List of all services on this system
on the network!
<not used any more>
/etc/protocols
/etc/services
What are we keeping track of?
Where are we storing it?
How do we see it?
gethostbyname(), gethostbyaddr()
getnetbyname(), getnetbyaddr()
getprotobyname(), getprotobynumber()
getservbyname(), getservbyport()

## Slide 108
There is, however, a little complication
The getyyybyxxx() routines return information in structures
gethostbyxxx() returns hostent
getservbyxxx() returns servent
getprotobyxxx() returns protoent
getnetbyxxx() returns netent

## Slide 109
Host Routines: Overview
Used to return host addresses from databases or name servers
Can query by host name
  DNS gurus: A records
Can query by address
  DNS gurus: PTR records
Returns everything in hostent structures

## Slide 110
Host Routines: Synopsis
#include <netdb.h>
struct hostent *gethostbyname(char *name);
/* returns pointer to an object describing an Internet host referenced by name */
struct hostent *gethostbyaddr(char *addr, int len, int type);
/* returns pointer to an object describing an Internet host referenced by address */
/* len = length of address */
/* type = type of address, should be AF_INET */

## Slide 111
hostent structure
A hostent structure (defined in <netdb.h>) which is:
struct hostent {
char *h_name: /* official name of host */
char **h_aliases; /* alias list */
int h_addrtype; /* host address type */
int h_length; /* length of each address */
char **h_addr_list; /* list of addresses */
};

## Slide 112
Service Routines: Overview
Used to convert service names (SMTP, POP, FTP, TELNET) to numbers
Also returns the preferred protocol for use with that service
Returns everything in servent structures

## Slide 113
Service Routines: Synopsis
#include <netdb.h>
struct servent *getservbyname(char *name, char *proto);
/* returns pointer to an object describing a service on the local machine referenced by name and protocol to be used */
struct servent *getservbyport(int port, char * proto);
/* returns pointer to an object describing a service on the local machine referenced by port and protocol number */
/* “proto” may be left null */

## Slide 114
servent structure
A servent structure is:
struct servent {
char **s_name; /* official service name */
char **s_aliases; /* alias list */
int s_port; /* port number, network byte order */
char *s_proto; /* protocol to use */
};

## Slide 115
Protocol Routines: Overview
Used to convert protocol names (IP, TCP, UDP) to numbers
Returns everything in protoent structures
Only ever used to be absolutely correct when calling socket() routines

## Slide 116
Protocol Routines: Synopsis
#include <netdb.h>
struct protoent *getprotobyname(char *name);
/* returns pointer to an object describing a protocol which may or may not be offered on the local machine, by name */
struct protoent *getprotobynumber(int proto);
/* returns pointer to an object describing a protocol which may or may not be offered on the local machine, by number */

## Slide 117
servent structure
A protoent structure is:
struct protoent {
char *s_name; /* official name of protocol */
char **p_aliases; /* alias list */
int p_proto; /* protocol number */
};

## Slide 118
Network Routines: Overview
Used to convert network names to numbers
Returns everything in netent structures
Never used any more

## Slide 119
Library Routines Key Concepts
Use byteorder routines (htonl, ntohl, etc.) to keep protocol headers straight
Use inet routines (inet_addr, inet_ntoa) to translate simple numeric strings to numbers
Use netdb routines (gethostbyname, etc.) to look up information in the network databases

## Slide 120
OpenVMS Specific Issues

## Slide 121
Using Sockets on VMS
Any application code can use sockets
Any language can use sockets (e.g. Tony McCraken’s Bare Bones Telnet BBTN program in MACRO-32)
Data structures and library routines pre-defined for the C language

## Slide 122
C Run-Time Integration
DEC has integrated support for sockets into VAX C and DEC C run-time libraries
Must use DEC TCP/IP Services (UCX) or emulation
Should use header files that come with VAX C/DEC C with this interface
Can use read() and write()

## Slide 123
TCPware’s Socket Library
DISCOURAGED! Be Vendor Neutral!
Pre-dates VAX C/DEC C API (and UCX)
Socket library provided as shareable image and object library

## Slide 124
MultiNet’s Socket Library
DISCOURAGED! Be Vendor Neutral!
Pre-dates VAX C/DEC C API (and UCX)
Socket library provided as shareable image
Not integrated with C RTL I/O subsystem
  Must use socket_read(), socket_write() and socket_close() on MultiNet sockets
  Separate socket_errno value and socket_perror() routine

## Slide 125
TCPware Header Files
Don’t use. Modern versions of DEC C include all the routines you need
Header files under TCPWARE_INCLUDE:

## Slide 126
MultiNet Header Files
Don’t use. Modern versions of DEC C include all the routines you need
Header files under MULTINET_ROOT:[MULTINET.INCLUDE]
  <sys/types.h> becomes MULTINET_ROOT:[MULTINET.INCLUDE.SYS]TYPES.H
  <resolv.h> becomes MULTINET_ROOT:[MULTINET.INCLUDE]RESOLV.H
There are bugs in the Multinet header files
  We warned you!

## Slide 127
Multinet - Easing the transition
You can ease the transition by defining logical names
  $ define inc multinet_root:[multinet.include.]/translation=concealed
  $ define sys inc:[sys],sys$share:
  $ define net inc:[net],sys$share:
  $ define netinet inc:[netinet],sys$share:
These are not needed for modern versions of DEC C; the compiler has it all figured out

## Slide 128
OpenVMS Specific Key Concepts
Don’t use Multinet or TCPware specific routines unless you have to
Portable sockets are usually the way to go
Session NM059 (4:00) will discuss when and how to use QIOs for VMS

## Slide 129
Session NM058 TCP Programming Example Joel Snyder Opus One

## Slide 130
Course Roadmap
NM055 (11:00-12:00) Important Terms and Concepts
  TCP/IP and Client/Server Model
  Sockets and TLI
  Client/Server in TCP/IP
NM056 (1:00-2:00) Socket Routines
NM057 (2:00-3:00) Library Routines
NM058 (3:00-4:00) Sample Client/Server
NM059 (4:00-5:00) VMS specifics (QIOs)
NM067 (6:00-7:00) Clinic - Q&A

## Slide 131
TCP/IP Programming
Slides and Source Code available via anonymous FTP:
Host:: ftp.process.com
Directory: [pub.decus]
Slides: DECUS_F96_PROG.PS
Examples: DECUS_F96_PROG_EXAMPLES.TXT
Host: ftp.opus1.com
Directory: [.decus]
Slides: DECUS_F96_PROG.POWERPOINT
Examples: DECUS_F96_PROG_EXAMPLES.TXT

## Slide 132
TCP Server Example
See handout

## Slide 133
TCP Client Example
See handout

## Slide 134
UDP Programming Example

## Slide 135
UDP Programming Example
We’ll create a datagram socket
We’ll fill in the important structures
We’ll explicitly bind()

## Slide 136
UDP Example - socket()
(1) Create an Internet Datagram socket (UDP)
/*
* Create an IP family socket on which to make the connection
*/
s=socket(hp->h_addrtype, SOCK_DGRAM, 0);
if(s<0){
socket_perror(“udpechoclient: socket”);
exit(0x10000000);
}

## Slide 137
UDP Example - sockaddr
(2) Fill in socket address structure
sp=getservbyname(“echo”,”udp”);
if(sp==NULL){
fprintf(stderr,”udpechoclient: echo/udp: unknown service\n”);
exit(0x10000000);
}
/*
* Creat a “sockaddr_in” structure which describes the remote
* IP address we want to sent to (from gethostbyname()) and
* the remote UDP port number (from getservbyname()).
*/
sin.sin_family = hp->h_addrtype;
memcpy(&sin.sin_addr, hp->h_addr, hp->h_length);
sin.sin_port=sp->s_port;

## Slide 138
UDP Example - sin.sin_addr
(3) Get address, parse, insert
  Protocol independent, same as TCP

## Slide 139
UDP Example - bind()
(4) Explicit bind, implicit connect
/*
* Do a psuedo-connect to that address. This tells the kernel
* that anything on this socket gets sent to this destination.
* It also binds us to a local port number (random, but that
* is ok).
*/
n=connect(s,&sin,sizeof(sin));
if(n<0){
socket_perron(“udpechoclient:connect”);
exit(0x10000004);
}

## Slide 140
UDP Example - socket_write()
(5) Write data out
  Protocol independent, just like TCP

## Slide 141
UDP Example - socket_read()
(6) Read data in
  Protocol independent, just like TCP

## Slide 142
Practical Troubleshooting

## Slide 143
Troubleshooting Tips
Network Byte Order
Watch out for the Terminator
Get return status from library routines

## Slide 144
Tips - Network Byte Order
“Big-endian” vs. “Little-endian” hosts
  VMS systems are little-endian
  TCP/IP uses big-endian order
htonl(), htons() convert host to network byte order
ntohl() and ntohs() are network to host conversions

## Slide 145
Tips - Terminators
TCP is a stream-oriented protocol
No such thing as a “record terminator”
You have to “roll your own”
  <CR><LF> is common for ASCII text protocols
  4 byte message length followed by message
  Fixed length message (rarely used)

## Slide 146
Use return status from library routines
Well, it’s there for a reason
It might tell you something
Failure usually means the opposite of success
  Typically it’s a data structure error
  make sure using perror() that it’s not a network problem

## Slide 147
Troubleshooting Tools
TCPDUMP displays packets
ECHO and DISCARD ports aid in debugging
$ UCX SHOW parameter
$ NETCU SHOW parameter (TCPware)
$ MULTINET SHOW/your_qualifier_here

## Slide 148
Using TCPDUMP
Limit your port
  $ multinet tcpdump/port=nn
Limit your hosts
  $ multinet tcpdump src hst my.host.here dst hst remote.host
Look at the inside of the packet
  $ multinet tcpdump/snapshot=1500/hexadecimal

## Slide 149
TCPware’s NETCU DEBUG
NETCU DEBUG/ (UDP,TCP,IP)
Limit your port
  $NETCU DEBUG/TCP/LPN=nn/FPN=nn
Limit your hosts
  $NETCU DEBUG/IP/SIA=host/DIA=x.x.x.x
Look at the packet headers
  $NETCU DEBUG/HEADER
Look at the inside of the packet
  $NETCU DEBUG/UDP/DATA=N

## Slide 150
Using the ECHO/DISCARD services
The echo service returns what you send it
The discard service eats what you send it
Start a TCPDUMP session
Have your clients talk to these ports
Have a TELNET client talk to your server
You can debug UDP by writing TCP code and modifying it to use datagrams

## Slide 151
TCPware $ NETCU SHOW/EVERYTHING
Network connection table
Route table
Services
Etc.

## Slide 152
TCPware Network Connections
Use $ NETCU show connection
ESTABLISHED shows for successful TCP connections
TIME_WAIT indicates remote side closed connection
CLOSE_WAIT indicates local side closed connection
See RFC-793 TCP state machine for more details

## Slide 153
TCPware Network Route Table
Use $ NETCU show route(/FULL)
If host routes with MTUs different from the interface form, MTU discovery may be in effect
Use NETCU/FULL to see Path MTU and network mask values
Variable Length Subnets supported

## Slide 154
$ MULTINET SHOW/EVERYTHING
Network connection table
Route table
MTU Discovery

## Slide 155
Network Connection Table
Use $multinet show/connection
ESTABLISHED shows for successful TCP connections
TIME_WAIT indicates remote side closed connection
CLOSE_WAIT indicates local side closed connection
See RFC-793 TCP state machine for more details

## Slide 156
Network Route Table
Use $ multinet show/route
If host routes with MTUs different from the interface form, MTU discovery may be in effect
  stop MTU discovery
    $ multinet set/kernel tcp_do_mtu_discovery 0 (3.3B and up)
  delete the route
    $ mu set/rout/delet=(dest:a.b.c.d,gate:a.b.c.d)
Create a host route and watch the usage grow!

## Slide 157
$ UCX SHOW/EVERYTHING
Network connection table
Route table
Device Sockets

## Slide 158
TCP/IP Programming Key Concepts
Use examples from similar applications that work
  “Steal” from the best
Suggested resources
  Curry, Donald A., Using C on the UNIX System, O’Reilly and Associates
  Comer, Douglas Internetworking with TCP/IP, Volume III, Prentice-Hall
  DEC C Run-Time Library Reference Manual (May, 1995 or later, Appendix A)
  MultiNet Programmer’s Guide

## Slide 159
Session NM059 TCP/IP Programming on VMS Geoff Bryant Process Software

## Slide 160
Course Roadmap
NM055 (11:00-12:00) Important Terms and Concepts
  TCP/IP and Client/Server Model
  Sockets and TLI
  Client/Server in TCP/IP
NM056 (1:00-2:00) Socket Routines
NM057 (2:00-3:00) Library Routines
NM058 (3:00-4:00) Sample Client/Server
NM059 (4:00-5:00) VMS specifics (QIOs)
NM067 (6:00-7:00) Clinic - Q&A

## Slide 161
TCP/IP Programming
Slides and Source Code available via anonymous FTP:
Host:: ftp.process.com
Directory: [pub.decus]
Slides: DECUS_F96_PROG.PS
Examples: DECUS_F96_PROG_EXAMPLES.TXT
Host: ftp.opus1.com
Directory: [.decus]
Slides: DECUS_F96_PROG.POWERPOINT
Examples: DECUS_F96_PROG_EXAMPLES.TXT

## Slide 162
Overview
TCP/IP Concepts
  TCP byte stream service
  UDP datagram service
  TCP or UDP? (how to choose)
Sockets vs. QIOs
Stream (TCP) Client calls
Stream (TCP) Server calls
Datagram (UDP) Client calls
Datagram (UDP) Server calls
Multithreaded servers

## Slide 163
TCP/IP Concepts
Networking services
  TCP - reliable byte stream service
  UDP - connectionless datagram service
  IP - connectionless datagram service
Naming communication endpoints
  Internet Addresses
  Port Numbers
  Servers contacted at well-known ports
    Ports 1 - 1023 are privileged port numbers
    Ports 1024 - 65535 are unrestricted
Sockets
  BSD Unix abstraction used to access the network
  Available in DECC Runtime Library
TCP
UDP
IP
Physical Network
Application

## Slide 164
IP - Internet Protocol
Lowest Layer of TCP/IP suite
Typically not used directly by application programs
Connectionless
“Unreliable” datagram service
  Low overhead
  Delivery of a datagram is not guaranteed
  Datagrams may be delivered out of order
  Duplicate datagrams may be received
Upper layer protocols implement reliability
Used by TCP and UDP
Host A
IP datagrams
Host B

## Slide 165
UDP - User Datagram Protocol
“Thin” Layer on top of IP (adds port concept)
Used directly by application programs
Like IP (low overhead, connectionless, unreliable)
Not reliable
  Client must retransmit request if no reply received
  Server may receive duplicate datagrams
Best for request/reply applications
Used by DNS, NFS, SNMP, RIP, etc....
Host A
UDP datagrams
Host B

## Slide 166
TCP - Transmission Control Protocol
Layered on top of IP
Adds port and byte stream concepts
Used directly by application programs
Connection oriented
Reliable byte stream service
  Delivery of bytes is guaranteed
  Bytes delivered in order
  No duplication of bytes
Used by FTP, TELNET, SMTP, etc....
TCP byte stream
Host A
Host B

## Slide 167
TCP - Transmission Control Protocol
TCP is a reliable BYTE STREAM protocol
  No one-to-one correspondence between send operations and receive operations
    Number of send operations may NOT be equal to the number of receive operations
    A receive operation may receive fewer bytes than was sent in a send operation
    A receive operation may receive data from several sends (more than one message may be received)
TCP does NOT do messages

## Slide 168
TCP - Transmission Control Protocol
Your application must implement messages
  Client/Server need to agree on and implement a message protocol:
    Messages separated by <CR><LF>
    Messages preceded by byte count length
    Messages of fixed length
  Choose TCP for applications which require reliable transmission
TCP does NOT do messages

## Slide 169
TCP or UDP - Which to use?
TCP
  Connection oriented, reliable byte stream
  More overhead than UDP
UDP
  Connectionless, unreliable, datagram service
  Less overhead than TCP
Choose TCP for applications which require reliable transmission
  File transfer (FTP)
  Virtual terminals (TELNET)
Choose UDP for:
  Simple request/reply applications (DNS)
  Applications which can tolerate unreliable transmission (Routing protocols such as RIP)

## Slide 170
Sockets vs. QIOs
Sockets
  Portable to other platforms
  Available via DEC C RTL
    3rd Party Socket Libraries
    Recommend DEC C RTL, supported by 3rd parties
$QIOs
  VMS only
  Can easily write asynchronous code
  Can easily write multithreaded servers
  BGDRIVER (Digital TCP/IP Services/UCX interface)
    3rd Party interfaces: INETDRIVER, TCPDRIVER, UDPDRIVER
    Recommend BGDRIVER, supported by 3rd parties

## Slide 171
$QIO Programming
SYS$ASSIGN to assign/create channel to device
SYS$QIO
  Queue an I/O request to device
  Asynchronous
  AST routine invoked on completion (Optional)
  Event Flag set on completion (Optional)
SYS$QIOW
  Synchronous - waits for completion
SYS$DASSGN to deassign/release channel

## Slide 172
$QIO Programming
SYS$QIO(EF,CHN,FUNC,IOSB,ASTADR,ASTARG,P1,...,P6)
  EF Optional Event Flag
  CHN Required Channel (SYS$ASSIGN)
  FUNC Required Function to perform
  IOSB Recommended I/O Status Block
  ASTADR Optional AST routine address
  ASTARG Optional AST parameter
  P1-P6 Opt/Req Function specific args

## Slide 173
BGDRIVER $QIO - Socket Equivalents
SOCKET()
BIND()
LISTEN()
ACCEPT()
CONNECT()
SEND()
RECV()
CLOSE()
GETxxBYyy
SYS$ASSIGN
SYS$QIO IO$_SETMODE
SYS$QIO IO$_SETMODE
SYS$QIO IO$_SETMODE
SYS$QIO IO$_ACCESS ! IO$M_ACCEPT
SYS$QIO IO$_ACCESS
SYS$QIO IO$_WRITEVBLK
SYS$QIO IO$_READVBLK
SYS$QIO IO$_DEACCES
SYS$DASSGN
SYS$QIO IO$_ACPCONTROL

## Slide 174
Stream (TCP) Client and Server
socket()
close()
write()
read()
accept()
listen()
bind()
connect()
write()
read()
close()
socket()
Client
connection
data (request)
data (reply)
Server

## Slide 175
Stream (TCP) Client
Create a network device ($ASSIGN BG0:)
Create a socket ($QIO IO$_SETMODE)
Open connection to the server ($QIO IO$_ACCESS)
  Specify internet address of server obtained from gethostbyname() or inet_addr
  Specify port number of server’s well-known port - obtained from getservbyname()
Send and receive data ($QIO IO$_WRITEVBLK and $QIO IO$_READVBLK)
Close the connection ($QIO IO$_DEACCESS)
Deallocate network device ($DASSGN)

## Slide 176
Stream (TCP) Client
Example client
  Program prompts user for server’s host name
  Looks up server’s internet address from host name
  Connects to server at port 65000
  Sends message to server
  Closes connection
#define SERVER_PORT 65000
/*
** UCX-compatible Stream (TCP) Client using BGDRIVER $QIOs
**
** To build against TCPware on VAX:
** $ CC/DEFINE=TCPWARE UCX_CLIENT
** $ LINK UCX_CLIENT,TCPWARE:UCX$IPC/LIB,SYS$INPUT/OPTIONS
** SYS$SHARE:VAXCRTL/SHARE
**
** To build against TCPware on AXP:
** $ CC/DEFINE=TCPWARE/STANDARD=VAXC UCX_CLIENT
** $ LINK UCX_CLIENT
**

## Slide 177
Stream (TCP) Client
** To build against UCX on VAX:
** $ CC UCX_CLIENT
** $ LINK UCX_CLIENT,SYS$LIBRARY:UCX$IPC/LIB,SYS$INPUT/OPTIONS
** SYS$SHARE:VAXCRTL/SHARE
**
** To build against UCX on AXP:
** $ CC/STANDARD=VAXC UCX_CLIENT
** $ LINK UCX_CLIENT
**
*/
#include <in.h>
#include <netdb.h>
#include <string.h>
#include <starlet.h>
#include <descrip.h>
#include <iodef.h>
#ifdef TCPWARE
#include "TCPWARE_INCLUDE:ucx$inetdef.h" /* Provided by TCPware install */
#else
#include <ucx$inetdef.h> /* Provided during UCX installation */
#endif

## Slide 178
Stream (TCP) Client
/*
** Macros to check VMS success/failure status
*/
#define SUCCESS(status) (status&1)
#define FAILURE(status) (!(status&1))
/*
** Values for boolean variables
*/
#define FALSE 0
#define TRUE 1
/******************************/
/* Client Program */
/******************************/
main() {
int status; /* For return status */
short channel; /* BG channel number */
short sck_parm[2]; /* Socket creation parameter */
short iosb[4]; /* I/O status block */
char buf[512]; /* buffer to transmit */
struct SOCKADDRIN remote_host; /* remote host's address & port */
struct hostent *he; /* returned from gethostbyname */
char server_name[256]; /* name of remote server */
int got_host; /* boolean */

## Slide 179
Stream (TCP) Client
/*
** UCX item list 2 descriptor used during $QIO IO$_ACCESS
*/
struct IL2 {
unsigned int il2_length;
char *il2_address;
} rhst_adrs = {sizeof remote_host, &remote_host};
/*
** String descriptor used during $ASSIGN
*/
struct dsc$descriptor inet_dev =
{10, DSC$K_CLASS_S, DSC$K_DTYPE_T, "UCX$DEVICE"};
/*
** Assign a channel to the UCX device.
*/
status = sys$assign( &inet_dev, &channel, 0, 0);
if (FAILURE(status)) {
printf("Failed to assign channel to UCX device.\n");
exit(status);
}

## Slide 180
Stream (TCP) Client
/*
** Prompt user for server name.
** Lookup the corresponding internet address.
*/
got_host = FALSE;
while( got_host == FALSE ) {
printf("Enter name of remote host:");
gets( server_name );
if ((he = gethostbyname( server_name )) == NULL)
printf("Error, gethostbyname failed\n");
else
got_host = TRUE;
}
memcpy((char *)&remote_host.SIN$L_ADDR, he->h_addr, he->h_length );

## Slide 181
Stream (TCP) Client
/*
** Create the socket
*/
sck_parm[0] = UCX$C_TCP; /* TCP/IP protocol */
sck_parm[1] = INET_PROTYP$C_STREAM; /* stream type of socket */
status = sys$qiow( 3, /* Event flag */
channel, /* Channel number */
IO$_SETMODE, /* I/O function */
iosb, /* I/O status block */
0, 0,
&sck_parm, 0, /* P1 Socket creation parameter */
0, 0,
0, 0);
if (SUCCESS(status)) status = iosb[0];
if (FAILURE(status)) {
printf("Failed to create and bind the device socket.\n");
exit(status);
}

## Slide 182
Stream (TCP) Client
/*
** Connect to specified host and port number
*/
remote_host.SIN$W_FAMILY = UCX$C_AF_INET; /* INET family */
remote_host.SIN$W_PORT = htons( SERVER_PORT ); /* port number */
status = sys$qiow( 3, /* Event flag */
channel, /* Channel number */
IO$_ACCESS, /* I/O function */
iosb, /* I/O status block */
0, 0,
0, 0,
&rhst_adrs, /* P3 Remote IP address */
0, 0, 0);
if (SUCCESS(status)) status = iosb[0];
if (FAILURE(status)) {
printf("Failed to connect to remote host.\n");
exit(status);
}

## Slide 183
Stream (TCP) Client
/*
** Send message to the server
**
** Note that this client/server combination implements
** a very simple message protocol - the client simply
** sends a text string of any size and then closes
** the connection. The server simply keeps reading
** (and printing the received text to SYS$OUTPUT)
** until the connection is closed by the client.
*/
strcpy( buf, "Hello there Mr. Server. Are you listening?");
status = sys$qiow( 3, /* Event flag */
channel, /* Channel number */
IO$_WRITEVBLK, /* I/O function */
iosb, /* I/O status block */
0, 0,
buf, /* P1 buffer */
strlen(buf), /* P2 buffer length */
0, 0, 0, 0);
if (SUCCESS(status)) status = iosb[0];
if (FAILURE(status))
printf("Failed to write to socket.\n");

## Slide 184
Stream (TCP) Client
/*
** Close the socket (optional - could just let $DASSGN
** perform the close)
*/
status = sys$qiow( 3,
channel,
IO$_DEACCESS,
iosb,
0, 0,
0, 0, 0, 0, 0, 0);
if (SUCCESS(status)) status = iosb[0];
if (FAILURE(status))
printf("Failed to close the socket.\n");
/*
** Deassign the UCX device channel.
*/
status = sys$dassgn( channel );
if (FAILURE(status))
printf("Failed to deassign the channel.\n");
}

## Slide 185
Stream (TCP) Client and Server
socket()
close()
write()
read()
accept()
listen()
bind()
connect()
write()
read()
close()
socket()
Client
connection
data (request)
data (reply)
Server

## Slide 186
Stream (TCP) Server
Create network device ($ASSIGN BG0:)
Create socket and bind to well-known port for the service ($QIO IO$_SETMODE)
  “Official” servers use getservbyname() to obtain assigned port number for the service
  Examples here use an unreserved port number
Put socket in listen mode ($QIO IO$_SETMODE)
Wait for and accept incoming connection
  Create new BG device for connection ($ASSIGN BG0:)
  Accept connection ($QIO IO$_ACCESS ! IO$M_ACCEPT)
  Original BG device continues listening for new connections

## Slide 187
Stream (TCP) Server
Receive and send data as needed for the service ($QIO IO$_READVBLK and IO$_WRITEVBLK)
Close the connection ($QIO IO$_DEACCESS)
Go to step 4
Deallocate the BG device ($DASSGN)

## Slide 188
Stream (TCP) Server
Example server
  Bind and listen at port 65000
  Accept incoming connection
  Read message sent by client
  Write message to SYS$OUTPUT
  Close connection
  Go back and accept next incoming connection

## Slide 189
Stream (TCP) Server
#define SERVER_PORT 65000 /* server's port number to use */
/*
**
** UCX-compatible Stream (TCP) Server using BGDRIVER $QIOs
**
** To build against TCPware on VAX:
** $ CC/DEFINE=TCPWARE UCX_SERVER
** $ LINK UCX_SERVER,TCPWARE:UCX$IPC/LIB,SYS$INPUT/OPTIONS
** SYS$SHARE:VAXCRTL/SHARE
**
** To build against TCPware on AXP:
** $ CC/DEFINE=TCPWARE/STANDARD=VAXC UCX_SERVER
** $ LINK UCX_SERVER
**
** To build against UCX on VAX:
** $ CC UCX_SERVER
** $ LINK UCX_SERVER,SYS$LIBRARY:UCX$IPC/LIB,SYS$INPUT/OPTIONS
** SYS$SHARE:VAXCRTL/SHARE
**
** To build against UCX on AXP:
** $ CC/STANDARD=VAXC UCX_SERVER
** $ LINK UCX_SERVER
*/

## Slide 190
Stream (TCP) Server
#include <in.h>
#include <string.h>
#include <starlet.h>
#include <descrip.h>
#include <iodef.h>
#include <ssdef.h>
#ifdef TCPWARE
#include "TCPWARE_INCLUDE:ucx$inetdef.h" /* Provided by TCPware install */
#else /* assume UCX */
#include <ucx$inetdef.h> /* Provided during UCX installation */
#endif
/*
** Macros to check VMS success/failure status
*/
#define SUCCESS(status) (status&1)
#define FAILURE(status) (!(status&1))
/*
** Values for boolean variables
*/
#define FALSE 0
#define TRUE 1

## Slide 191
Stream (TCP) Server
main() {
int status; /* For return status */
short listen_chan; /* Listening device's channel */
short con_chan; /* Accepted connection's channel */
short sck_parm[2]; /* Socket creation parameter */
short iosb[4]; /* I/O status block */
char buf[512]; /* buffer for received data */
int buflen = 512; /* buffer length */
unsigned char *ria; /* remote host's internet address */
int r_retlen; /* length of remote host name structure */
int connected; /* boolean */
/*
** Socket name structures for local and remote endpoints
** (filled in during IO$_ACCESS|IO$M_ACCEPT)
*/
struct SOCKADDRIN local_host, remote_host;
/*
** UCX item list 2 descriptor used for local host name
** (filled in during IO$_ACCESS|IO$M_ACCEPT)
*/
struct IL2 {
unsigned int il2_length;
char *il2_address;
} lhst_adrs = {sizeof local_host, &local_host};

## Slide 192
Stream (TCP) Server
/*
** UCX item list 3 descriptor used for remote host name
** (filled in during IO$_ACCESS|IO$M_ACCEPT)
*/
struct IL3 {
unsigned int il3_length;
char *il3_address;
unsigned int il3_retlen;
} rhst_adrs = {sizeof remote_host, &remote_host, &r_retlen};
/*
** String descriptor used during $ASSIGN BG0:
*/
struct dsc$descriptor inet_dev =
{10, DSC$K_CLASS_S, DSC$K_DTYPE_T, "UCX$DEVICE"};
/*
** Socket options item list (used during IO$_SETMODE that
** creates the listen socket to set the REUSEADDR option)
*/
int optval = 1; /* option value = 1 means turn it on */
struct { short len, param; int *ptr; }
item_list[] = {{sizeof(optval), UCX$C_REUSEADDR, &optval}},
options = {sizeof(item_list), UCX$C_SOCKOPT, item_list};

## Slide 193
Stream (TCP) Server
/*
** Assign a channel for the listen socket.
*/
status = sys$assign(&inet_dev, &listen_chan, 0, 0);
if (FAILURE(status)) {
printf("Failed to assign channel to UCX device.\n");
exit(status); }
/*
** Create the listen socket and set the REUSEADDR option.
*/
sck_parm[0] = UCX$C_TCP; /* TCP protocol */
sck_parm[1] = INET_PROTYP$C_STREAM; /* stream type of socket */
status = sys$qiow( 3, /* Event flag */
listen_chan, /* Channel number */
IO$_SETMODE, /* I/O function */
iosb, /* I/O status block */
0, 0,
&sck_parm, 0, /* P1 Socket creation parameter */
0, 0,
&options, 0); /* P5 Socket option descriptor */
if (SUCCESS(status)) status = iosb[0];
if (FAILURE(status)) {
printf("Failed to create the device socket.\n");
exit(status); }

## Slide 194
Stream (TCP) Server
/*
** Bind and listen to specified port number (after REUSEADDR is set above).
*/
local_host.SIN$W_FAMILY = UCX$C_AF_INET; /* INET (TCP/IP) family */
local_host.SIN$L_ADDR = UCX$C_INADDR_ANY; /* any address */
local_host.SIN$W_PORT = htons( SERVER_PORT ); /* server's port # */
status = sys$qiow( 3, /* Event flag */
listen_chan, /* Channel number */
IO$_SETMODE, /* I/O function */
iosb, /* I/O status block */
0, 0,
0, 0,
&lhst_adrs, /* P3 local socket name */
5, /* P4 Connection backlog */
0, 0);
if (SUCCESS(status)) status = iosb[0];
if (FAILURE(status)) {
printf("Failed to bind the device socket.\n");
exit(status); }
else
printf("Port is bound and listening\n");

## Slide 195
Stream (TCP) Server
/******************************************************/
/* Main server loop */
/* 1. accept new connection */
/* 2. read message from client */
/* 3. print message to SYS$OUTPUT */
/* 4. close connection */
/* 5. go to step 1 */
/*****************************************************/
while ( 1 ) { /* sit in this loop forever (break with CTRL-Y) */
/*
** Assign channel for the new connection
*/
status = sys$assign(&inet_dev, &con_chan, 0, 0);
if (FAILURE(status)) {
printf("Failed to assign channel for accept.\n");
exit(status);
}

## Slide 196
Stream (TCP) Server
/*
** Accept a connection from a client.
*/
status = sys$qiow( 3, /* Event flag */
listen_chan, /* listen channel number */
IO$_ACCESS|IO$M_ACCEPT, /* I/O function */
iosb, /* I/O status block */
0, 0,
0, 0,
&rhst_adrs, /* P3 Remote IP address*/
&con_chan, /* P4 Channel for new socket */
0, 0);
if (SUCCESS(status)) status = iosb[0];
if (FAILURE(status)) {
printf("Failed to accept a connection from a client.\n");
exit(status); }
/*
** Print out the connecting client's internet address & port
*/
ria = &remote_host.SIN$L_ADDR;
printf("Connection from host: %d.%d.%d.%d, port: %d\n",
ria[0], ria[1], ria[2], ria[3],
htons(remote_host.SIN$W_PORT));

## Slide 197
Stream (TCP) Server
/*
** Read data from client (and write it to SYS$OUTPUT)
** until client closes it's end of the connection
**
** Note that this client/server combination implements
** a very simple message protocol - the client simply
** sends a text string of any size and then closes
** the connection. The server simply keeps reading
** (and printing the received text to SYS$OUTPUT)
** until the connection is closed by the client.
**
** Recall that the TCP byte-stream does NOT guarantee
** a one-to-one correspondence of client writes to server
** reads, so you may see several reads for the client's
** single write. (With the short message used here,
** you probably won't, but you might.)
*/
connected = TRUE;
while ( connected ) {

## Slide 198
Stream (TCP) Server
/*
** Read I/O buffer
*/
status = sys$qiow( 3, /* Event flag */
con_chan, /* Channel number */
IO$_READVBLK, /* I/O function */
iosb, /* I/O status block */
0, 0, /* no AST, no AST parm */
buf, /* P1 buffer */
buflen, /* P2 buffer length */
0, 0, 0, 0);
if (SUCCESS(status)) status = iosb[0];
if (FAILURE(status)) {
if (status != SS$_LINKDISCON ) { /* SS$_LINKDISCON indicates normal termination */
printf("Failed to read from socket.\n");
printf("iosb[0] = 0x%x\n", iosb[0] );
printf("iosb[1] = 0x%x\n", iosb[1] ); }
connected = FALSE; /* terminate while loop */ }
else {
/* All is well, print message */
buf[iosb[1]] = '\0'; /* make sure message is null-terminated */
printf ("Received text: %s\n", buf); }
} /* end of connected while loop */

## Slide 199
Stream (TCP) Server
/* ** Shut down the socket that was connected to the client
** and deassign the channel used with that socket. */
status = sys$qiow( 3,
con_chan,
IO$_DEACCESS|IO$M_SHUTDOWN,
iosb,
0, 0,
0, 0, 0,
UCX$C_DSC_ALL, /* P4 Discard all packets */
0, 0 );
if (SUCCESS(status)) status = iosb[0];
if (FAILURE(status))
printf("Failed to shut down the client socket.\n");
status = sys$dassgn(con_chan);
if (FAILURE(status))
printf("Failed to deassign the client socket.\n");
printf("FYI: Port is still bound and listening...\n");
} /* end of main while loop */
/*
** Note: We don't explicitly shutdown the listen socket
** and deassign the listen channel. This will be done
** during image run-down whey you CTRL-Y EXIT the program
*/
}

## Slide 200
Datagram (UDP) Client and Server
close()
sendto()
recvfrom()
connect()
sendto()
recvfrom()
close()
bind()
Client
data (request)
data (reply)
socket()
bind()
socket()
retransmit?
Server

## Slide 201
Datagram (UDP) Client
Create network device ($ASSIGN BG0:)
[Optional] “Connect” to server ($QIO IO$_ACCESS)
  UDP is connectionless
  Simply specifies communication endpoint for send
Send a request datagram ($QIO IO$_WRITEVBLK)
Start a timer
Receive reply datagram ($QIO IO$_READVBLK)
  If timer expires during receive, repeat at step 3
If more to request, go to step 3
Close and deallocate network device ($QIO IO$_DEACCESS followed by $DASSGN)

## Slide 202
Datagram (UDP) Server
Create network device ($ASSIGN BG0:)
Bind network device to well-known port ($QIO IO$_SETMODE)
Wait for request ($QIO IO$_READVBLK)
Send reply ($QIO IO$_WRITEVBLK)
Go to step 3

## Slide 203
More Sophisticated Servers
Multithreaded Servers
  Use ASTs (or Event Flags)
  One thread for each connection
  Must maintain “context block” for each connection

## Slide 204
More Sophisticated Servers
Server started by INET Master Server (inetd)
  On UCX this is a “UCX auxiliary server”
  One server process per connection
    Easily supports multiple connections
    Costs a VMS process
  Add server information to inetd database
  Server automatically started when connection request comes in to host
    UCX master server invokes .COM or .EXE
    Server’s input, output, error files assigned to BG device
    Maser server does “socket”,”bind”,”listen”,”accept”

## Slide 205
References
Internetworking with TCP/IP, Volume III: Client-Server Programming and Applications (BSD Socket Version), Douglas E. Comer and Richard L. Stevens, Prentice-Hall, Inc. 1993. ISBN #0-13-474222-2
Internetworking with TCP/IP, Volume I, Principles, Protocols, and Architecture, @3rd ed., Douglas E. Comer, Prentice-Hall, Inc. 1995. ISBN #0-13-468505-9
DEC TCP/IP Services for OpenVMS system Services and C Socket Programming manual
  Documentation for BG and socket routines
DEC OpenVMS System Services Reference manual
  SYS$ASSIGN, SYS$QIO(W), SYS$DASSGN
Programming manuals for 3rd party TCP/IP stacks
  When using UCX emulation, usually only need compile and link information; otherwise use DEC TCP/IP Services manuals

## Slide 206
TCP/IP Programming
Slides and Source Code available via anonymous FTP:
Host: ftp.process.com
Directory: [pub.decus]
Slides: DECUS_F96_PROG.PS
Examples: DECUS_F96_PROG_EXAMPLES.TXT
Host: ftp.opus1.com
Directory: [.decus]
Slides: DECUS_F96_PROG.POWERPOINT
Examples: DECUS_F96_PROG_EXAMPLES.TXT