## Slide 1
DECUS Session IN028 Wednesday May 21, 1997 TCP/IP Programming: Introduction
Geoff Bryant
bryant@process.com
©1997 Process Software
Notes: 1

## Slide 2
Slides available via anonymous FTP:
Host: ftp.process.com
Directory: [pub.decus.spring_97]
Slides: IN028_prog_intro.ps
IN028_prog_intro.ppt

## Slide 3
The OSI Network Model
Physical
Data Link
Network
Transport
Session
Presentation
Application
Transmission of binary data of a medium
Transfer of units of information, framing, and error checking
Delivery of packets of information, which includes routing
Provision for end-to-end reliable and unreliable delivery
Establishment and maintenance of sessions
Data formatting and encryption
Network applications such as file transfer and terminal
emulation

## Slide 4
The TCP/IP Protocol Layers
Network Device Drivers
Network Device Drivers
Network Protocols/Drivers
TCP
UDP
IP (ICMP)
Network Device Drivers
Network Device Drivers
Network Controllers
Ethernet or other physical medium
FTP
Telnet
Ping
NFS
Traceroute
Notes: 7

## Slide 5
TCP/IP Network Layers
Physical
Data Link
Network
Transport
Session
Presentation
Application
Transmission of binary data of a medium
ARP
IP
TCP and UDP
Network applications such as file transfer and terminal
emulation

## Slide 6
Protocol Layering
Each layer adds information as data is passed down to lower layers
  Added information almost always added as header
Each layer removes its information as data is passed up to higher layers
Application Data
Application Data
Application Data
Application Data
Application Data
Application Data
Application Data
Application Data
TCP
TCP
IP
TCP
IP
Network
TCP
IP
Network
TCP
IP
TCP
Physical network
Sending Data
Receiving Data
Notes: 9

## Slide 7
The TCP/IP Protocol Layers
Network Device Drivers
Network Device Drivers
Network Protocols
TCP
UDP
IP (ICMP)
Network Device Drivers
Network Device Drivers
Network Controllers
Ethernet or other physical medium
FTP
Telnet
Ping
NFS
Traceroute
Notes: 10

## Slide 8
Network Protocols
Responsible for sending and receiving IP datagrams over local network
Responsible for mapping internet addresses into physical addresses
  Ethernet/FDDI use Address Resolution Protocol (ARP)
  Internet address mapped is for the next hop the datagram will visit - might not be ultimate destination for the datagram
Notes: 11

## Slide 9
The TCP/IP Protocol Layers
Network Device Drivers
Network Device Drivers
Network Protocols
TCP
UDP
IP (ICMP)
Network Device Drivers
Network Device Drivers
Network Controllers
Ethernet or other physical medium
FTP
Telnet
Ping
NFS
Traceroute
Notes: 13

## Slide 10
IP - Internet Protocol
Connectionless datagram service
Performs:
  Routing
  Fragmentation/Reassembly
“Unreliable”: Does not perform
  Flow Control
  Sequence Control
  Duplicate Avoidance
  Error Recovery
High Performance and Low Overhead
Notes: 12

## Slide 11
Internet Addresses
Uniquely identifies an interface within a network
Syntax: a.b.c.d (x:y::z and ::a.b.c.d for IPv6)
32 bit number (128 bits for IPv6)
  Network number (used for routing)
  Host number
  In “classfull” routing, host bits can used for subnet
Address classes
  A: 1.h.h.h through 127.h.h.h, Network Mask: 255.0.0.0
  B: 128.0.h.h through 191.255.h.h, Network Mask: 255.255.0.0
  C: 192.0.0.h through 223.255.255.h, Network Mask: 255.255.255.0
  D,E: 224.0.0.0 and higher (multicast and reserved)
Notes: 14

## Slide 12
IP Datagram
Vers
Len
TOS
Total Length
Identification
Flags
Fragment Offset
TTL
Protocol
Header Checksum
Source Internet Address
Destination Internet Address
Options...
Padding
Data...
0
4
8
16
19
24
31
Field Purpose
Vers IP version number
Len Length of IP header (4 octet units)
TOS Type of Service
T. Length Length of entire datagram (octets)
Ident IP datagram ID (for frag/reassembly)
Flags Don’t/More fragments
Frag Off Fragment Offset
Field Purpose
TTL Time To Live - Max # of hops
Protocol Higher level protocol (1=ICMP,
6=TCP, 17=UDP)
Checksum Checksum for the IP header
Source IA Originator’s Internet Address
Dest IA Final Destination Internet Address
Options Source route, timestamp, etc.
Notes: 15

## Slide 13
Network-Byte Order
Big-Endian & Little-Endian
  Network: Big
  VAX, Alpha, Intel: Little
Integer Conversion:
  htons: Host-to-Net (short)
  htonl: Host-to-Net (long)
  ntohs: Net-to-Host (short)
  ntohl: Net-to-Host (long)
IP Address
TCP & UDP Port
Low
00000000
High
00000010
High
00000010
Byte #N
Low
00000000
Byte #N+1
Big-Endian
Byte Order
Little-Endian
Byte Order
Notes: 16

## Slide 14
The TCP/IP Protocol Layers
Network Device Drivers
Network Device Drivers
Network Protocols
TCP
UDP
IP (ICMP)
Network Device Drivers
Network Device Drivers
Network Controllers
Ethernet or other physical medium
FTP
Telnet
Ping
NFS
Traceroute
Notes: 17

## Slide 15
UDP - User Datagram Protocol
Connectionless unreliable datagram service
  Adds port concept to identify peer application
  Datagrams may be lost, out of order, or duplicated
  Very low overhead
Used by applications such as TFTP, DNS, RPC
  Best for simple transaction oriented requests
Advantages over using IP directly
  Can address individual applications via well-known ports
  Checksums (pseudo IP header, UDP header, Data)
Notes: 18

## Slide 16
UDP datagram
Destination Port
Source Port
Application data
0
16
31
Checksum
Length
Field Purpose
Source Port 16-bit port number identifying originating application
Destination Port 16-bit port number identifying destination application
Length Length of UDP datagram (UDP header + data)
Checksum Checksum of IP pseudo header, UDP header, and data
Notes: 19

## Slide 17
The TCP/IP Protocol Layers
Network Device Drivers
Network Device Drivers
Network Protocols
TCP
UDP
IP (ICMP)
Network Device Drivers
Network Device Drivers
Network Controllers
Ethernet or other physical medium
FTP
Telnet
Ping
NFS
Traceroute
Notes: 20

## Slide 18
TCP - Transmission Control Protocol
End-to-end reliable, connection-oriented
  Byte-stream protocol, not message oriented
  Data delivered in order with no duplication
  Flow controlled
  Full duplex
Uses ports to identify individual connections and applications
  Servers contacted at well-known ports
  Well-known port numbers assigned by IANA (Internet Assigned Numbers Authority)
Notes: 21

## Slide 19
TCP - Transmission Control Protocol
Provides reliability
  Handles damaged, lost, duplicated, and out of sequence data
  Uses positive acknowledgments
  Time-outs indicate negative acknowledgment
  Each data octet (and SYN and FIN control bits) are assigned a sequence number
Notes: 22

## Slide 20
TCP does NOT do messages
TCP is a reliable BYTE STREAM protocol
  No one-to-one correspondence between send operations and receive operations
    Number of send operations may NOT be equal to the number of receive operations
    A receive operation may receive fewer bytes than was sent in a send operation
    A receive operation may receive data from several sends (more than one message may be received)
Notes: 23

## Slide 21
TCP does NOT do messages
Your application must implement messages
  Client/Server need to agree on and implement a message protocol:
    Messages separated by <CR><LF>
    Messages preceded by byte count length
    Messages of fixed length
  Choose TCP for applications which require reliable transmission
Notes: 24

## Slide 22
TCP Connection Flow
Server prepares to receive connections (passive open)
  Creates SOCKET
  BINDs to well known port
  Tells TCP layer to LISTEN for connections
  ACCEPTs incoming connection
Client initiates connection (active open)
  Creates SOCKET
  CONNECTs to server
Data is transmitted and received by client/server
Client and Server CLOSE/SHUTDOWN connection
Notes: 25

## Slide 23
TCP Connection States
CLOSED
BEGIN/socket()
LISTEN
Server Passive Open
bind(),listen(),accept()
Close()
SYN SENT
Active Open
send SYN
Client Active Open connect()
send SYN
SYN RCVD
rcv SYN
send SYN,ACK
rcv SYN
send SYN,ACK
rcv RST
ESTABLISHED
rcv ACK of SYN
rcv SYN,ACK
send ACK
FIN WAIT-1
FIN WAIT-2
CLOSE_WAIT
CLOSING
TIME_WAIT
LAST_ACK
Close()
send FIN
rcv ACK
rcv FIN
send ACK
timer ~ 1 min
rcv FIN,ACK
send ACK
rcv FIN
send ACK
rcv ACK
Close() send FIN
rcv FIN
send ACK
Close()
send FIN
rcv ACK
Close()
Notes: 26

## Slide 24
TCP Segment
Destination Port
Acknowledgment Number
Options...
Padding
Data...
0
4
10
16
19
24
31
Source Port
Window
Len
Sequence Number
Reserved
Flags
Urgent Pointer
Checksum
Field Purpose
Source Port Identifies originating application
Destination Port Identifies destination application
Sequence Number Sequence number of first octet in the segment
Acknowledgment # Sequence number of the next expected octet (if ACK flag set)
Len Length of TCP header in 4 octet units
Flags TCP flags: SYN, FIN, RST, PSH, ACK, URG
Window Number of octets from ACK that sender will accept
Checksum Checksum of IP pseudo-header + TCP header + data
Urgent Pointer Pointer to end of “urgent data”
Options Special TCP options such as MSS and Window Scale
Notes: 27

## Slide 25
Why “Client/Server?”
Rendezvous...
  Can you imagine the difficulty of two programs starting simultaneously on two different hosts so they can “talk together?”
  With several millisecond-long execution times, synchronizing each one at their (respective) correct execution sequence is a tricky job!
Client/Server
  One side starts and waits for the other side to contact it:
    “Server” waits ...
    “Client” initiates...
Notes: 28

## Slide 26
References
Internetworking with TCP/IP, Volume III: Client-Server Programming and Applications (BSD Socket Version), Douglas E. Comer and David L. Stevens, Prentice-Hall, Inc. 1993. ISBN #0-13-474222-2
Internetworking with TCP/IP, Volume I, Principles, Protocols, and Architecture, @3rd ed., Douglas E. Comer, Prentice-Hall, Inc. 1995. ISBN #0-13-468505-9
Notes: 154

## Slide 27
Slides available via anonymous FTP:
Host: ftp.process.com
Directory: [pub.decus.spring_97]
Slides: IN028_prog_intro.ps
IN028_prog_intro.ppt